## Slide 1: Best practice in numerical simulation and CFD benchmarking. Results from the SUSANA project
Tolias, I.C.1, Giannissi, S.G.1, Venetsanos, A.G.1, Keenan, J.2, Shentsov, V. 2, Makarov, D. 2, Coldrick, S.3, Kotchourko, A.4, Ren, K.4, Jedicke, O.4, Melideo, D.5, Baraldi, D.5, Slater, S.6, Duclos, A.7, Verbecke, F.7 and Molkov, V. 2
1 Environmental Research Laboratory, National Centre for Scientific Research Demokritos, Agia Paraskevi, Athens, 15310, Greece, tolias@ipta.demokritos.gr
2 HySAFER Centre, Ulster University, Newtownabbey, BT37 0QB, UK, dv.makarov@ulster.ac.uk
3 Health and Safety Executive, Harpur Hill, Buxton, SK17 9JN, UK, Simon.Coldrick@hsl.gsi.gov.uk
4 Karlsruhe Institute for Technology (KIT), Kaiserstrasse 12, Karlsruhe, Germany, olaf.jedicke@kit.edu
5 European Commission, Joint Research Centre (JRC), IET, Westerduinweg 3, 1755 LE, Petten, Netherlands, daniele.baraldi@ec.europa.eu
6 Element Energy Limited, Station Road 20, Cambridge, United Kingdom, shane.slater@element-energy.co.uk
7 Areva Stockage d'Energie SAS, Batiment Jules Verne, Domaine du Petit Arbois, Aix-en-Provence, France, audrey.duclos@areva.com

## Slide 2: Introduction
SUSANA: SUpport to SAfety ANalysis of Hydrogen and Fuel Cell Technologies (www.support-cfd.eu) Aim: Support stakeholders who use Computational Fluid Dynamics (CFD) for safety engineering design and assessment of FCH systems and infrastructure
  State-of-the-art in physical and mathematical modelling
  Guide to Best Practice in use of CFD for safety analysis
  Verification and validation procedures
  Benchmarking
  HYMEP (Baraldi et al. 2017)

## Slide 3: Benchmarking
Improve the numerical modelling of realistic accident scenarios in hydrogen industry
  Comparison of the different methodologies against experiments
  Analysis of the suitability of the models for each specific physical process
  Inter comparisons of the different methodologies
All phenomena are covered
  Release and dispersion
  Ignition
  Jet fires
  Deflagrations
  Detonations
Notes: The aim of the benchmarking is..

## Slide 4: Best Practice Guidelines
To apply CFD properly and to provide accurate results, CFD users should follow the correct modelling strategy
A number of Best Practice Guidelines (BPG) for CFD applications have been developed for this purpose in the past
  General BPG for industrial CFD simulations (ERCOFTAC, 2000)
  CFD in urban environment (COST, 2007)
  CFD in nuclear reactor safety applications (OECD, 2007)
  Ventilation and gas dispersion in gas turbine enclosures (Ivings et al., 2003)
No BPG for hydrogen

## Slide 5: Best Practice Guidelines
Produce a comprehensive publicly available Best Practice Guide on the application of the CFD methodology for safety analysis of Fuel Cells and Hydrogen (FCH) installations/ technology
Provide support on the correct application of the CFD methodology to
  CFD users (industry/research) and stakeholders (industry/regulating officials)
  Other on-going hydrogen safety related projects
The reader is introduced to the appropriate modelling approach and by following this, improve the accuracy and fidelity of their modelling

## Slide 6: Best Practice Guidelines
Chapters of BPG (all related phenomena are covered)
  Chapter 0: Introduction
  Chapter 1: Hydrogen release and dispersion
  Chapter 2: Ignition and jet fires
  Chapter 3: Deflagrations
  Chapter 4: Detonations
  Chapter 5: CFD User Education and Training
  Chapter 6: Appendix (Sample Cases)
Structure of each Chapter (all aspects of CFD simulations are covered)
  Selection of physical models
  Problem setup (geometry, mesh, initial and boundary conditions)
  Numerical options (solver type, spatial and temporal discretization schemes, convergence criteria)
  Analysis of the simulation results (validation, sensitivity and interpretation of the results)
Total number of pages: 235
Notes: Covers all related phenomena: release, dispersion, ignition, fire, deflagration, detonation
All general aspects of CFD simulations

## Slide 7: Best Practice Guidelines
General BPG
  High quality mesh (expansion factor, cell aspect ratio, cell skewness)
    Enhance accuracy and assist numerical convergence
  Grid independency study
    At least three different grid sizes should be tested
    Ideally, each finer grid should have double the number of cells
  Computational domain
    Domain boundaries should be located far enough in order to minimize the impact of the boundary conditions on the results, e.g. away from vents
    A domain size sensitivity study should be performed
  Time step
    Sensitivity study (a factor of two smaller time is recommended)
    LES: small time step sizes corresponding to CFL<1 are suggested
Notes: A grid independence study is very important because results with coarse grids can be misleading

## Slide 8: Best Practice Guidelines
General BPG
  Numerical scheme
    High-order accuracy numerical schemes are recommended in order to decrease numerical diffusion - necessary for complex flows such as impinging jets and deflagrations
    LES: central differences schemes because upwind-biased schemes suppress turbulence
    Scalar conservation equation: Total Variation Diminishing (TVD) scheme should be used in order to ensure a bounded solution
Notes: A grid independence study is very important because results with coarse grids can be misleading

## Slide 9: Release and dispersion: Best Practice Guidelines
High-pressure jet releases
  For practical applications involving high pressure releases (above 1.9 times Patm) notional nozzle approaches, are recommended:
    Reasonable results avoiding the high computational cost of resolving directly the complex flow structure near the nozzle
    For low storage pressures the approach of Birch et al. (1987) can be applied
    For high storage pressures (above 10-20 MPa) where the ideal gas assumption becomes less valid, the Schefer et al. (2007) or Molkov et al. (2009) are recommended
    Modelling the transient blowdown from a storage vessel requires a transient implementation of the notional nozzle approach

## Slide 10: Release and dispersion: Best Practice Guidelines
Liquid hydrogen (LH2)
  Isenthalpic or isentropic expansion can be assumed to estimate the flashed vapor fraction at the inlet
  Various modelling approaches:
    Mixture approach
      Thermal equilibrium between phases => phase distribution using Raoult’s law
      Conservation equations for the mixture and total hydrogen mass (vapour + liquid) with or without slip velocities
    Multi-fluid approach
      Separate conservation equations for each phase
  Heat transfer modelling from the ground is important for LH2 releases near ground (film boiling phenomena)
  Ambient air humidity condensation and nitrogen, oxygen liquefaction due to cryogenic temperatures may affect hydrogen dispersion

## Slide 11: Release and dispersion: Benchmark
Benchmark experiment: KIT (Veser et al. 2011)
  Cryo-compressed hydrogen
  Horizontal jet releases in closed facility
Simulation (Venetsanos & Giannissi 2017):
  Sensitivity studies: Domain size, CFL number, number of cells
  3rd order numerical scheme (QUICK)
  Birch (1987) notional nozzle approach
  Good agreement with the experiment
Veser, A., Kuznetsov, M., Fast, G. et al., The structure and flame propagation regimes in turbulent hydrogen jets, Int. J. Hydrogen Energy, 36 (3), 2011, 2351-59
Venetsanos, A.G., Giannissi, S.G., Release and dispersion modeling of cryogenic under-expanded hydrogen jets, Int. J. Hydrogen Energy, 42 (11), 2017, 7672-82

## Slide 12: Ignition and jet fire: Best Practice Guidelines
Sudden release of hydrogen gas from a high pressure reservoir Auto-ignition Jet fire
Auto-ignition modelling: Simulation of shocks, small scale turbulent mixing and shock wave/vortex interactions
  Very dense mesh
  Highly accurate numerical methods
  Various strategies of modelling
    2D DNS or LES models: Limited to simplified axi-symmetrical geometry.
    3D LES models:
      More realistic geometries
      Accurate combustion models, such as EDC with detailed chemistry

## Slide 13: Ignition and jet fire: Best Practice Guidelines
Jet fire modelling
  Under-expanded jets for compressed hydrogen
    Notional nozzle approach
  Combustion modelling
    Simplified EBU/EDM models
      limited to well-ventilated fires
    Flamelet model
    EDC with detailed chemistry
      more accurate
      larger computational requirements

## Slide 14: Ignition and jet fire: Benchmark
Spontaneous ignition in Pressure Relief Device (PRD), (Bragin et al. 2013)
  LES modelling
  EDC with detailed chemistry
  Step-like approximation of the membrane burst process
External domain
High pressure tubes
Burst disk
PRD
Bragin, M.V., Makarov, D.V. and Molkov, V.V., Pressure limit of hydrogen spontaneous ignition in a T-shaped channel, Int. J. Hydrogen Energy, 38, No. 19, 2013, pp. 8039–8052

## Slide 15: Ignition and jet fire: Benchmark

## Slide 16: Deflagration: Best Practice Guidelines
Unfortunately, there is no modelling approach which is clearly superior to all others and applicable to all circumstances
  complex interactions between the turbulent flow field and combustion chemistry
  Instabilities (Darrieus-Landau, Rayleigh-Taylor e.t.c.)
  very wide-range of applications (open deflagrations, vented deflagration, congestion)
BPG
  The self-similar flame acceleration should be addressed in the model
  Vented deflagration: accurate prediction of the intensity of the external explosion
  Obstacles which influence the flame but are too small (PDR - Porosity Distributed Resistance models)
  Non-uniform concentration
    Equivalent uniform stoichiometric volume method

## Slide 17: Deflagration: Benchmark
FM-Global experiment
  Dimensions 4.6×4.6×3.0 m
  Central ignition, 5.4 m2 vent
  Simulation using four codes
    ADREA-HF
    FLUENT
    FLACS
    CFX

## Slide 18: Detonation: Best Practice Guidelines
Detonation modelling
  Arrhenius law: The reaction zone must be resolved. Large number of cells must be placed inside it.
  Heaviside detonation model: A specific model designed for under-resolved simulations, in which space resolution requirements cannot be satisfied, as it happens in most engineering and safety simulations
    It assumes an infinitively fast chemical reaction
  LES model based on progress variable equation
    Does not require detailed chemistry
    Detonation velocity can be pre-calculated
Computational cell size depends on the choice of chemical model:
  Detailed chemistry model: 1 to 10 µm
  One step Arrhenius model: 1 mm
  Heaviside model: 0.1 m

## Slide 19: Detonation: Benchmark
Detonation’s cellular structures
Deflagration to Detonation Transition (DDT)
  MINI RUT experiment

## Slide 20: Conclusions
BPGs in numerical simulations for Fuel Cells and Hydrogen applications were briefly presented
Focus on the practical needs of engineers in consultancies and industry undertaking CFD simulations in support of hazard/risk assessments of hydrogen facilities, and the needs of regulatory authorities
BPG application through a series of CFD example cases were also presented for each phenomenon (dispersion, ignition, deflagration, detonation), in order to provide a demonstration of their application

## Slide 21: Ευχαριστώ! (Thank you)
The authors would like to thank the SUSANA project, which has received funding from the European Union's Seventh Framework Programme (FP7/2007-2013) for the Fuel Cells and Hydrogen Joint Technology Initiative under grant agreement n°FCH-JU-325386.
www.support-cfd.eu