## Slide 1: Evaluation of an improved vented deflagration CFD model against nine experimental cases
Tolias, I.C.1, Venetsanos, A.G.1, Kuznetsov, M.2
1Environmental Research Laboratory, National Centre for Scientific Research Demokritos, Agia Paraskevi, Athens, 15341, Greece
2Institute of Nuclear and Energy Technologies, Karlsruhe Institute of Technology, Hermann-von-Helmholtz-Platz 1, 76344, Eggenstein-Leopoldshafen
tolias@ipta.demokritos.gr

## Slide 2: Introduction
Hydrogen
  Significant reductions in greenhouse gas emissions
  Significant improvements in energy efficiency
Accidental release in closed space catastrophic consequences in the case of an explosion
  Much higher over-pressure compared open space
A way of mitigation: Vents
Computational Fluid Dynamics (CFD)
  Attractive methodology for risk assessment: Accurate modelling of the geometry and the flow
  Turbulent combustion difficulties: Very large range of scales
    Models are needed

## Slide 3: Introduction
The aim of the work is the improvement of a CFD model and the evaluation against vented deflagration experiments.
Vented deflagrations
  Many overpressures peaks may appear
    opening of the vent
    external explosion
    instabilities due to flame-acoustic interaction

## Slide 4: CFD model
Deflagration model: LES with Multi-phenomena turbulent burning velocity model (Molkov 2012)1
Gradient method:
Turbulent flame speed:
  Ξk : Turbulence generated by the flame front itself
  Ξlp : Leading point concept – preferential diffusion
  Ξf : Increase of flame surface due to its fractal geometry
Promising model which, however, fails to reproduce external explosion in vented deflagrations
1Molkov, V., Fundamentals of Hydrogen Safety Engineering II, BookBoon, 2012

## Slide 5: CFD model
Changes made in the original model1:
  Account for subgrid scale phenomena (instabilities)
    No modification of the laminar burning velocity
    Wrinkling factors Ξ multiply the turbulent flame velocity
  Turbulent flame speed: Schmid’s equation2 instead of Yakhot’s equation3
    More recent relation which account for Damköhler number
  Turbulence approach: k-ε model (Kato, Launder 1993)4 instead of LES
    Less strict requirements of k-ε model in terms of grid and numerical schemes
4Kato M, Launder BE. The modeling of turbulent flow around stationary and vibrating square cylinders. In: Ninth Symp. Turbul. Shear Flows, Kyoto, Japan, 16-18 August, 1993
3Yakhot V., 1988, Propagation Velocity of Premixed Turbulent Flames. Combust Sci Technol, 60, 191–214
2Schmid H-P, Habisreuther P, Leuckel W. A, 1998, Model for Calculating Heat Release in Premixed Turbulent Flames. Combust Flame, 113, 79–91
1Tolias I.C., Venetsanos A.G., 2018, An improved CFD model for vented deflagration simulations – Analysis of a medium-scale hydrogen experiment, IJHE, 43 (52), 23568-84
Initial model
New model
Notes: We performed the following changes in the model in order to improve its accuracy:
The first change is about how we account for the subgrid scale phenomena.
We do not modify the laminar burning velocity in the turbulent burning velocity relation. As a result the impact of turbulence on the flame remains unchanged.
In order to account for the instabilities, the Ξ factors multiples the turbulent flame velocity and not the laminar one like in the initial model.

## Slide 6: Experiments
KIT medium scale vented experiment (Kuznetsov et al. 2015)1,2
  0.94 m3 enclosure (0.98 x 0.96 x 1.0 m)
  Vent 0.5 x 0.5 m2
  18.0 % v/v hydrogen-air homogeneous mixture
  Back-wall ignition
  Pressure measurement inside & outside the enclosure
1Kuznetsov, M., et al. (2015), Medium-scale experiments on vented hydrogen deflagration, Journal of Loss Prevention in the Process Industries, 36, 416-428
2HyIndoor project, Pre-normative research on safe indoor use of fuel cells and hydrogen Systems, www.hyindoor.eu

## Slide 7: Experiments
Experimental overpressure

## Slide 8: Simulation set-up
ADREA-HF CFD code
  Navier-Stokes equations + Continuity equation
  Energy equation (conservation equation of total enthalpy)
  Conservation equations of mass fractions
  k-ε turbulence model (Kato & Launder modification)
Numerical details
  Bounded second order upwind method
  CFL=0.2, fully implicit first order scheme
  Stagnant initial flow field, very low values of k and ε (1.0e-06)
  Three computational grids:
    714,000 cells (dx=0.03 m)
    1,539,000 cells (dx=0.02 m)
    2,726,000 cells (dx=0.015 m)

## Slide 9: Simulation results
Grid independency study

## Slide 10: Simulation results
Comparison with experiment

## Slide 11: Experiments
FM-Global experiments in a real scale room (Bauwens et al.)1,2,3
  63.48 m3 enclosure (4.6 x 4.6 x 3.0 m)
  Vent 5.4 x 5.4 m2
  Back-wall or central ignition
Two groups of experiments
  18.0 % v/v hydrogen-air homogeneous mixture (2 cases)
    Back ignition
    Central ignition
  15.0 % v/v hydrogen-air homogeneous mixture with initial turbulence (6 cases)
    Back ignition: 3 cases of initial turbulence
    Central ignition: 3 cases of initial turbulence
1Bauwens CR, Chaffee J, Dorofeev SB., 2011, Vented explosion overpressures from combustion of hydrogen and hydrocarbon mixtures. Int J Hydrogen Energy, 36, 2329–36.
2Bauwens CR, Dorofeev SB. Hydrogen Vented Deflagrations at FM Global: Tests and Modeling. Presentation in “Advanced Research Workshop: Progress in safe indoor use of fuel cells and hydrogen systems”, September 12th, 2013.
3Bauwens CR, Dorofeev SB., 2014, Effect of initial turbulence on vented explosion overpressures from lean hydrogen–air deflagrations. Int J Hydrogen Energy, 39,20509–15.

## Slide 12: Simulation set-up
ADREA-HF CFD code
  Same equations and numerical parameters like previous simulation
  Symmetry was assumed
  Two computational grids:
  395,560 cells (dx=0.150 m)
  893,412 cells (dx=0.100 m)

## Slide 13: Simulation results – 18% FM-Global cases
Grid independency study

## Slide 14: Simulation results – 18% FM-Global cases
Back ignition: 14% underprediction

## Slide 15: Simulation results – 18% FM-Global cases
Center ignition: 32% overprediction

## Slide 16: Simulation results – 15% FM-Global cases
Modelling of initial turbulence: A single constant factor was added1, ΞT0
1Bauwens CR, Dorofeev SB., 2014, Effect of initial turbulence on vented explosion overpressures from lean hydrogen–air deflagrations. Int J Hydrogen Energy, 39,20509–15.
u’ (m/s) | ΞT0
0.12 | 1.00
0.40 | 1.12
0.50 | 1.17

## Slide 17: Simulation results – 15% FM-Global cases
Center ignition cases
Overprediction 30-61 %
The deviations from the experiments in the central ignition cases are likely to be partially caused by the omission of a vent cover opening model
1Bauwens CR, Dorofeev SB., 2014, Effect of initial turbulence on vented explosion overpressures from lean hydrogen–air deflagrations. Int J Hydrogen Energy, 39,20509–15.

## Slide 18: Conclusions
A newly developed CFD model for vented deflagration simulations was presented.
Very good qualitative performance in most cases.
  New model predicts the violence of the external explosion very accurately
Very good performance for the back ignition cases: Maximum deviation of max. overpressure equal to 17%.
In central ignition cases, the model overpredicted the maximum overpressure up to 61%.
  Vent opening may have a more considerable impact on these cases.
Initial turbulence: it was reproduced successfully by applying only a constant factor in the burning velocity.
Physics of the phenomenon:
  Inside the enclosure: flame instabilities
  Outside the enclosure: turbulence

## Slide 19: Ευχαριστώ! (Thank you)
Acknowledgements: This Publication is supported by the program of Industrial Scholarships of Stavros Niarchos Foundation, Greece. The authors would like to gratefully thank Dr. Regis Bauwens for providing experimental data for the FM-Global experiments.
Questions

## Slide 20: Simulation set-up
Combustion parameters
  Hydrodynamic instability: