## Slide 1: ID154： Near-term location of hydrogen refueling stations in Yokohama city from the perspective of safety
Fuse, M.1, Kawanishi, N.1,Noguchi, H.1, and Seya, H2
1Graduate School of Engineering, Hiroshima University
2Graduate School of Engineering, Kobe University
International Conference on Hydrogen Safety
September, 24-26 2019, Adelaide (Australia)
This study was funded by the Japan Science and Technology Agency (JST), and the Cross-ministerial Strategic Innovation Promotion Program (SIP).

## Slide 2
Hydrogen Refueling Stations in Japan
Needs for near-term location plan of safe hydrogen refueling station at city level
Fuel cell vehicles (FCVs)
Hydrogen refueling stations (HRSs)
Toward a hydrogen economy in Japan
200,000 FCVs by 2025 (3,000 FCVs in 2019)
320 HRSs by 2025 (100 HRSs in 2019)
National level road map by METI
Hydrogen refueling station in Kofu, Japan
© Iwatani Corporation
Social acceptance; the neighbor’s objection
Safety of hydrogen refueling station
Introduction
Notes: As well know で水素は危険性をもつ

## Slide 3
Previous Studies and Aim
Introduction
HRS Location study
Demand-based approach
Supply-based approach
Supply-Demand approach
P-median model
Flow interception model
Travel time
Life cycle cost for supply
This study: safety perspectives
The aim is to plan the HRS locations over the years 2020–2030 in Yokohama City.
Notes: As well know で水素は危険性をもつ

## Slide 4
Yokohama City in Japan
Method
3.7 million people, big industrial zone and port, and 4 stationary and 2 mobile HRSs
A city at the forefront of Japan's push toward a hydrogen economy
Notes: As well know で水素は危険性をもつ

## Slide 5
Approach in planning hydrogen station locations
Method
Safety
Notes: As well know で水素は危険性をもつ

## Slide 6
Demand Model
Method
FCV demand at neighborhood level
Passenger vehicle demand
Replacement rate
to FCV from FCV
Optimistic scenario
Pessimistic scenario
Intermediate scenario
P: Population
FCV demand at city level
Allocation from city level to neighborhood level
HV: Hybrid Vehicles
Notes: As well know で水素は危険性をもつ

## Slide 7
Demand Model Parameters
Method
 | Passenger vehicle ownership model | Hybrid vehicle replacement rate model (Optimistic scenario) | Electric vehicle replacement rate mode (Pessimistic scenario)
a | 6.4 | 790 | 170
b | -0.0031 | -0.39 | 0.000043
c |  | 0.25 | -0.17
R2 | 0.96 | 0.98 | 0.99
n | 14, 2004-2017 | 20, 1998-2017 | 20, 1998-2017
Optimistic scenario: FCVs has the similar demand trend of hybrid vehicles.
Pessimistic scenario: FCVs has the similar demand trend of electric vehicle.
Neighborhood level trend of FCVs has the same as that of hybrid vehicles.
Model Assumptions
Estimation Results of Model Parameters
Notes: As well know で水素は危険性をもつ

## Slide 8
Supply Model
Method
Model Assumptions
HRS type:
  Off-site-type stationary
  300 Nm3
  70MPa
  900 FCVs
Area: 700 m2 by the safety regulations in Japan
Candidate place: surplus areas of gas stations
Surplus areas of gas stations in Yokohama City
Model Results
327 gas stations in Yokohama
95 HRS candidates with over 700 m2 surplus areas
HRS candidates
Notes: As well know で水素は危険性をもつ

## Slide 9
Supply-Demand Matching
Method
GIS superimposing analysis
Estimation data on FCV demand at Neighborhood level
Location data on HRS candidate
Calculate FCV demand of circles with radius 500 m around HRSs
Spatial distribution of circles around gas stations
In the case of radius 500 m
Matching rule
Select HRSs in descending order of FCV demand (highest first) until reaching the maximum HRS
To avoid the overlapping, the selection is conducted by each ward (18 wards in Yokohama City).
Notes: As well know で水素は危険性をもつ

## Slide 10
Number of Fuel Cell Vehicles owned in Yokohama
Results
Notes: As well know で水素は危険性をもつ

## Slide 11
Hydrogen Refueling Stations in Yokohama, Optimistic Scenario
Results
Notes: As well know で水素は危険性をもつ

## Slide 12
Hydrogen Refueling Stations in Yokohama, Intermediate Scenario
Results
Notes: As well know で水素は危険性をもつ

## Slide 13
Hydrogen Refueling Stations in Yokohama, Pessimistic Scenario
Results
Notes: As well know で水素は危険性をもつ

## Slide 14
Optimistic Scenario Location in Yokohama, 2030
Results
FCV demand at neighborhood level
Location of HRSs
Notes: As well know で水素は危険性をもつ

## Slide 15
Intermediate Scenario Location in Yokohama, 2030
Results
FCV demand at neighborhood level
Location of HRSs
Notes: As well know で水素は危険性をもつ

## Slide 16
Pessimistic Scenario Location in Yokohama, 2030
Results
FCV demand at neighborhood level
Location of HRSs
Notes: As well know で水素は危険性をもつ

## Slide 17
Conclusion
This study planned the location of hydrogen refueling stations (HRSs) in Yokohama City from 2020 to 2030, from the safety perspectives.
In this near-term plan, the existing HRSs could supply the FCVs up to 2024, and after that, the new HRS installations depend on the future scenarios.
In the long-term plan, the limitations in supplying the HRS supply will occur due to the luck of gas stations with a large surplus area.
Revisiting regulations on safety buffer zones and designing more compact HRS are options to mitigate the limitations in the planning.
The suggestions for revisiting safety regulations and designing compact HRS based on acceptable risk are future works.
Summary
Findings
Future works
Notes: As well know で水素は危険性をもつ

## Slide 18
Thank you very much for your attention !
masa-fuse@hiroshima-u.ac.jp

## Slide 19
Japan Hydrogen & Fuel Cell Demonstration Project, The report of JHFC Phase 2: FY2006-2010,
Notes: As well know で水素は危険性をもつ