## Slide 1: Paper-ID: 229 EXPERIMENTS ON THE COMBUSTION BEHAVIOUR OF HYDROGEN-CARBON MONOXIDE-AIR MIXTURES
A. Friedrich, G. Necker, G. Stern, A. Veser, J. Grune (Pro-Science)
M. Kuznetsov, T. Jordan (KIT)
Supported by:

## Slide 2
Introduction
Safety Considerations & Experimental Set-up
Test Procedure
Experiments in the Explosion Bomb
Summary
Outline

## Slide 3
Introduction
General Aim & Project Partners
In severe nuclear reactor accidents with core meltdown high pressure and temperature loads to the safety containment can occur, which might lead to local leakages of hydrogen and carbon monoxide formed due to the reaction of molten core and water or concrete. In such cases flammable H2-CO-air mixtures are generated in adjacent air-filled compartments.
For the evaluation of the damage potential that is associated with such scenarios and as a basis for the development of mitigation measures the combustion behavior of such stratified H2-CO-air layers in semi-confined geometries has to be investigated.
In this two-phase joint research project of PS/KIT with the Chair of Thermodynamics at the Technical University of Munich (TUM) the combustion properties of H2-CO-air mixtures are investigated with the aim to create a new scientific basis for the analysis of H2-CO-combustions in compartments outside the containment of a nuclear power plant.
In the first part of the current project Pro-Science performed small scale experiments in an explosion bomb to determine experimentally fundamental burning characteristics of H2-CO-air-mixtures.

## Slide 4
Gas-cylinder cabinet (CO)
H2- Bundle
Control room
Vessel V4
Chimney
Vessel exhaust
Safety Considerations & Experimental Set-up
Safety considerations and preparation of the bomb facility
Explosion bomb installed to safety vessel V4 at hydrogen test site HYKA at KIT (Dim. V4 [m]: di x H: 3.3 x 3.1  V = 21.5 m³, pstat: 40 bar)
Due to the acute toxicity of CO extended safety concept necessary:
All components bearing CO (except gas cylinder) housed in safety vessel,
During operation continuous ventilation through exhaust (580 m³/h (≈ 0.5 air-changes/min)) in a height of 6 m,
CO-sensor in safety vessel,
Access to vessel only with personalized CO-sensor,
CO-cylinder in outdoor cabinet with CO-sensor.
Explosion bomb

## Slide 5
pdynamic
P
P
T
T
Air
H2
Air
CO
Chimney
V09
V08
V06
V07
V01
V02
Explosion- bomb
V10
V11
V12
pstatic
V03
P
Gas-analysis
V04
V05
V13
CO
H2
Mixing- chamber
Massflow
Massflow
Massflow
Filling via 3 massflow-controllers for H2, CO and Air (Bronkhorst, Series F), and mixing chamber,
Spherical bomb:
di = 25 cm (V = 8.2 dm³),
pstatMax = 800 bar,
Tmax = 300 °C
Gas cylinders for H2 and CO, air from compressed air grid at KIT,
Static pressure sensor for vacuum and pressure control (Leybold, DI 2001, 0 – 2000 mbar),
Gas-analysis: Sensors for H2 and CO (Messkonzept, FTC 300, 0 – 100 Vol% H2, Sensors Europe, S-AGM Plus, 0 – 35 Vol% CO),
Vacuum-pump for evacuation of bomb and lines,
Experimental Set-Up
Bomb equipped with 2 dynamic pressure sensors (fine & coarse) and 2 thermocouples,
Vacuum pump
Ignition electrodes
Ignition electrodes.
Safety Considerations & Experimental Set-up

## Slide 6
Chimney
Vacuum pump
Air
Gas-analysis
pdynamic
pstatic
Massflow
Massflow
Massflow
H2
Air
CO
V10
V11
V12
V09
V08
V06
V07
V01
V02
V03
V04
V05
V13
P
CO
H2
P
P
T
T
Explosion- bomb
Mixing- chamber
Test procedure
Evacuation of bomb, mixing-chamber and pipe system,
Safety Considerations & Experimental Set-up

## Slide 7
Chimney
Vacuum pump
Air
Gas-analysis
pdynamic
pstatic
Massflow
Massflow
Massflow
H2
Air
CO
V10
V11
V12
V09
V08
V06
V07
V01
V02
V03
V04
V05
V13
P
CO
H2
P
P
T
T
Explosion- bomb
Mixing- chamber
Test procedure
Evacuation of bomb, mixing-chamber and pipe system,
Adjustment of desired mixture during bypass- flow via mixing-chamber and chimney,
Safety Considerations & Experimental Set-up

## Slide 8
Chimney
Vacuum pump
Air
Gas-analysis
pdynamic
pstatic
Massflow
Massflow
Massflow
H2
Air
CO
V10
V11
V12
V09
V08
V06
V07
V01
V02
V03
V04
V05
V13
P
CO
H2
P
P
T
T
Explosion- bomb
Mixing- chamber
Test procedure
Evacuation of bomb, mixing-chamber and pipe system,
Adjustment of desired mixture during bypass- flow via mixing-chamber and chimney,
Filling of bomb with mixture up to slight overpressure (approx. 1200 mbar),
Safety Considerations & Experimental Set-up

## Slide 9
Chimney
Vacuum pump
Air
Gas-analysis
pdynamic
pstatic
Massflow
Massflow
Massflow
H2
Air
CO
V10
V11
V12
V09
V08
V06
V07
V01
V02
V03
V04
V05
V13
P
CO
H2
P
P
T
T
Explosion- bomb
Mixing- chamber
Test procedure
Evacuation of bomb, mixing-chamber and pipe system,
Adjustment of desired mixture during bypass- flow via mixing-chamber and chimney,
Filling of bomb with mixture up to slight overpressure (approx. 1200 mbar),
Mixing-chamber and bypass are purged with air, simultaneously analysis of bomb content during depressurization to 1000 ±10 mbar,
Safety Considerations & Experimental Set-up

## Slide 10
Chimney
Vacuum pump
Air
Gas-analysis
pdynamic
pstatic
Massflow
Massflow
Massflow
H2
Air
CO
V10
V11
V12
V09
V08
V06
V07
V01
V02
V03
V04
V05
V13
P
CO
H2
P
P
T
T
Explosion- bomb
Mixing- chamber
Test procedure
Evacuation of bomb, mixing-chamber and pipe system,
Adjustment of desired mixture during bypass- flow via mixing-chamber and chimney,
Filling of bomb with mixture up to slight overpressure (approx. 1200 mbar),
Mixing-chamber and bypass are purged with air, simultaneously analysis of bomb content during depressurization to 1000 ±10 mbar,
Ignition,
Ignition electrodes
Safety Considerations & Experimental Set-up

## Slide 11
Chimney
Vacuum pump
Air
Gas-analysis
pdynamic
pstatic
Massflow
Massflow
Massflow
H2
Air
CO
V10
V11
V12
V09
V08
V06
V07
V01
V02
V03
V04
V05
V13
P
CO
H2
P
P
T
T
Explosion- bomb
Mixing- chamber
Test procedure
Evacuation of bomb, mixing-chamber and pipe system,
Adjustment of desired mixture during bypass- flow via mixing-chamber and chimney,
Filling of bomb with mixture up to slight overpressure (approx. 1200 mbar),
Mixing-chamber and bypass are purged with air, simultaneously analysis of bomb content during depressurization to 1000 ±10 mbar,
Ignition,
Evacuation of bomb, mixing-chamber and pipe system.
Safety Considerations & Experimental Set-up

## Slide 12
During the campaign the special lamp failed (irreparable), so a new lamp on LED-basis was developed,
With this lamp the experiments, especially on weak mixtures, were completed.
High-speed videography
In roughly half of the experiments a high-speed camera and a shadowgraphy system was used, Photron FASTCAM-SA1.1, max. res.: 1024 x 1024 Pixel (1,05 Megapixel) @ max. 5,4 kHz, max. frame rate: 675 kHz @ 64 x 16 Pixel
Safety Considerations & Experimental Set-up

## Slide 13
 Lower Flammability Limit
Experiments in the Explosion Bomb
Test-Matrix
Approximately 400 Ignition attempts were performed, but in more than 120 of these attempts no ignition was observed.

## Slide 14
Experiments in the Explosion Bomb
Lower Flammability Limit
Flammability limits of the binary mixtures: H2-air: 4,0 Vol% CO-air: 12,2 Vol%
The reaction of a dry CO-O2 mixture is very slow even at high temperatures, but the overall reactivity is greatly accelerated in the presence of trace amounts of moisture or H2,
But in the bomb experiments dry air was used to generate the mixture and thus no ignition of CO-air mixtures without H2 was possible,
In first tests an experiment was stopped when no ignition was observed in the first attempt,
In later experiments (with HS-camera) up to 4 (rarely 5) ignition attempts with increasing ignition duration (0.1 s up to > 2 s) were performed,
Mixture was labelled “unignitable” when all 4 attempts did not show any sign of ignition (neither in pressure nor in HS-video-record),

## Slide 15
Experiments in the Explosion Bomb
Lower Flammability Limit
Size of green dots (and number in brackets) indicates number of attempts needed to ignite the mixture,
H2-air mixtures could not be ignited below 5.2 Vol%,
Pure CO-air mixtures (without H2) could not be ignited at all,
Comparison with values calculated using
Le Chatelier’s Mixing Law for Flammability Limits
shows larger differences for yCO > 0.8.

## Slide 16
Experiments in the Explosion Bomb
SS: visible flame velocity SL: laminar flame velocity
B2: coefficient p0: initial pressure
γb/γu: cp/cv burned, unburned σ: expansion ratio (ρu/ρb),
rb: radius of burned gas R: radius of bomb
Kuznetsov et al. Laminar burning velocities of hydrogen-oxygen-steam mixtures at elevated temperatures and pressures, Proc. Comb. Inst. 33(2011) 895-903
Laminar Burning Velocities (Pressure Method) (no correction of stretch and instabilities possible)

## Slide 17
Experiments in the Explosion Bomb
Laminar Burning Velocities (Pressure Method)
Pressure increase in initial phase is due to (almost) spherical propagation of flame front,
So ∆p α t³ and thus representation of p1/3 over t should yield a straight line.

## Slide 18
Experiments in the Explosion Bomb
Laminar Burning Velocities (Pressure Method)
Set p(t=0) = 0 and plot p(t)1/3 over t, pressure record used up to p = 0,02 * pmax,
Linear regression, where slope yields B2, and intercept yields t0,
Problem: Result is dependent on range of regression!
Experiment
Fit
Regression

## Slide 19
Reasons:
  late ignition (recording time for P1 already over)
  quenching ( only experiments with pmax(Exp) ≥ 80% pAICC were used)
  irregular combustion  poor quality of regression (only evaluations with a goodness of fit R² > 0.99 were used)
Experiments in the Explosion Bomb
Laminar Burning Velocities (Pressure Method)
It was not possible to determine the laminar burning velocity for all tests with ignition,
Difficulties during evaluation especially for lean mixtures.

## Slide 20
Evaluation of shadowgraphy HS-movies
Determination of the burning velocity by tracking the circular flame front in the HS-videos
3 Examples (framing rate: 10.000 frames/s)
Experiments in the Explosion Bomb
HSCO-013
12 Vol% H2 in air
HSCO-188
6 Vol% H2 + 6 Vol% CO in air
HSCO-059
2 Vol% H2 + 10 Vol% CO in air

## Slide 21
Evaluation of shadowgraphy HS-movies
Principle
Circle was drawn on the borderline of the bubble, increase in radius over time yields velocity,
depending on necessity contrast is normalized or enhanced in image series (using Imagej),
in case method is applicable similar velocities as for pressure method were determined.
Experiments in the Explosion Bomb
Original image
Background subtracted and normalized
Problems
image noise
flame front sometimes hardly visible
flame shows no regular shape in diffuse borderline,
quenching of flame.

## Slide 22
Laminar burning velocities
Experiments in the Explosion Bomb
Results of series with pure H2-air mixtures could be compared with data from literature and formula published by Dong et al. (2009) for fuel rich mixtures,
Only few data for H2-CO-air mixtures available for evaluation of the method used, most useful:
  Dong et al. (2009): stoichiometric H2-CO-air mixtures with various H2/CO-ratios
Good agreement observed for both comparisons.
Dong C.et al.; Experimental study on the laminar flame speed of hydrogen/carbon monoxide/air mixtures, Fuel 88 (2009) 1858–1863

## Slide 23
Experiments in the Explosion Bomb
Laminar Burning Velocities (pressure method)
Laminar flame velocities of the mixtures decrease with increasing CO-fraction in the fuel,
Decrease from values for pure H2-air-mixtures (yCO = 0) to values for pure CO-air-mixtures, decrease can be linearly approached
Only few SL-values for CO available, so equation by Dong et al. (2009) was used,
Equation was derived for high CO-concentrations (>22 Vol%), utilization of equation down to 12 Vol% led to increasing deviations of approximation in CO rich mixtures especially for cFuel < 16 Vol%,
More accurate values for laminar burning velocity of pure CO-air mixtures would help to increase the accuracy of the proposed approximation.

## Slide 24
Summary
The authors are very grateful to the German Federal Ministry for Economic Affairs and Energy (BMWi) for funding (Project No. 1501545B), and also to the partners from the Chair of Thermodynamics at the Technical University of Munich (TUM) for fruitful discussions and support in the current work.
The experimental investigation on the combustion behavior of H2-CO-air-mixtures up to the stoichiometric composition (approx. 30 Vol% fuel in air) was performed using a bomb facility with pressure measurements and a high-speed shadowgraphy system at KIT,
Analysis of experimental data showed that Le Chatelier's mixing rule for lower flammable limits of mixtures can be used as conservative measure to determine the LFL of H2-CO-air mixtures,
For a wide range of fuel concentrations with various H2/CO ratios laminar burning velocities were determined and compared successfully with literature data, if available,
An easy-to-use correlation was proposed for estimation of laminar burning velocities for different mixture compositions using the laminar burning velocities of the two fuel components of the mixture,
The current work shows that CO-fractions in H2-air mixtures can neither be neglected nor treated as H2, since both, addition of CO and replacement of H2 by CO in H2-air mixtures have an influence on the combustion behavior of the mixture.
Thank you for your attention!