## Slide 1
2019/09/26
Effect of expansion ratio on flame acceleration during hydrogen fueled gas explosions
Jun Yaguchi, Wookyung Kim,
Toshio Mogi and Ritsu Dobashi
Department of Chemical System Engineering
The University of Tokyo

## Slide 2: Introduction
A precise understanding of the flame turbulence is indispensable to perform an appropriate risk assessment of hydrogen fueled gas explosion.
Due to prevalence of hydrogen use, the appropriate assessment of hydrogen fueled gas explosion is needed.
Flame surface is wrinkled spontaneously.
Flame speed is accelerated.
The intensity of blast wave is increased.[2]
Cellular flame (propane/air)[1]
[2] A. Thomas, et al, Flame noise: Sound emission from spark-iginited bubbles of combustible gas, Pro. Roy. Soc. A294, 449- 466 (1966).
[1] Kim, W., Mogi, T., Kuwana, K., Dobashi, R., Self-similar propagation of expanding spherical flames in large scale gas explosions, Proceedings of the Combustion Institute 35, 2051-2058 (2015)
Flame surface area is increased.

## Slide 3: Introduction - Flame front instabilities[3, 4]
[3] F. A. Williams, Combustion Theory : Second Edition, Westview Press (1985).
[4] D. Bradley, et al., Flame acceleration due to flame-induced instabilities in large-scale explosions, Combustion and Flame 124, 2001, pp. 551-559
Diffusional-thermal instability
caused by the preferential diffusion for non-equidiffusive mixtures
From small scale
Darrieus-Landau instability
From large scale
The effect on the self-acceleration is remarkable.
There are few data of large-scale experiments.
The research topic of the present study
caused by the thermal volumetric expansion of burned gas
Two instabilities induce flame turbulence spontaneously.

## Slide 4: Reserch contents
Investigation of the effect of the volumetric expansion ratio ε on DL instability
Objective
Experimental conditios
ε =
The density of burned gas
The density of unburned gas
H2 /O2-N2-Ar mixed gas
O2 : (N2+Ar) = 21 : 79
ε was changed by changing N2/Ar ratio
O2
N2
Ar
↔
H2
and
Small ε
Large ε
Ar concentration / (Ar+N2concentration) [-]
6.5
7.0
7.5
8.0
0
0.2
0.4
0.6
0.8
1
The volumetric expansion ratio
ε [-]
 = 1.0

## Slide 5: Reserch contents
Laboratory – scale experiments
Soap bubble
Experimantal methods
Large – scale experiments
Plastic tent
Soap bubble
5 cm
0.5 m
Flame
Plastic tent
The effect of scale was investigated.

## Slide 6: Experimental apparatus of laboratory-scale
Mercury
lamp
Schlieren mirror
Schlieren mirror
Knife edge
Electrodes
High speed camera
Microphone
Oscilloscope
Pressure
gauge
O2
H2
Mixing
chamber
Valve
N2
Vacuum pump
Amplifier
Ar
Igniter
Soap bubble
Computer
Pulse
generator
10 cm
1 m
Nozle
Imaging and recording with shlieren photography
t = 0.8 ms
t = 2.4 ms
t = 7.4 ms
t =9.8 ms
Soap bubble
5 cm

## Slide 7: Experimental apparatus of large-scale
Piezoelectoric
pressure sensor
H2
O2
Ar
Pulse
Generator
Monochrome
high speed camera
Electrodes
Computer
Oscilloscope
Igniter
Circulaton
pump
Gas concentration
measuring instrument
Plastic tent
3 m
1 m
1 m
1 m
recording
0 ms
2 ms
5 ms
9 ms
14 ms
0.5 m
Plastic tent

## Slide 8: Results and discussions（Laboratory-scale）
Dimensionless burning velocity VS Dimensionless flame radius
✔
Both diffusional-thermal and DL instability were not observed.
vb : Burning velocity（measured value） [m/s]
ε : volumetric expansion ratio [-]
r : Flame radius [mm]
SL : Unstreched burning velocity [m/s]
δ : Laminar flame thickness [mm]
r/δ [-]
vb/SL [-]
ε = 6.99, N2
ε = 7.88, Ar
0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
1.6
1.8
0
50
100
150
 = 1.0
Flame acceleration
Flame propagation
is not accelerated.
Dimensionless burning velocity
Dimensionless flame radius,
SL , δ, ε: calculated with CHEMKIN

## Slide 9: Results and discussions（Large-scale）
✔
The flame acceleration by DL instability was observed.
The flame acceleration at both of volumetric expansion ratios was almost the same.
✔
Dimensionless burning velocity VS Dimensionless flame radius
SL , δ, ε: calculated with CHEMKIN
vb : Burning velocity（measured value） [m/s]
ε : volumetric expansion ratio [-]
r : Flame radius [mm]
SL : Unstreched burning velocity [m/s]
δ : Laminar flame thickness [mm]
ε = 7.13, N2
ε = 8.06, Ar
0
1
2
3
4
0
400
800
1200
1600
 = 1.0
Flame acceleration
vb/SL [-]
r/δ [-]
Flame propagation
is not accelerated.
Dimensionless burning velocity
Dimensionless flame radius,

## Slide 10: Results and discussions（Large-scale）
The effect of ε on rc
✔ ε ↑ … rc↓
An increase in ε promoted the onset of DL instability.
0
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
Critical flame radius, rc [cm]
ε = 7.13, N2
ε = 8.06, Ar
 = 1.0
rc : critical flame radius [cm]
The transition point to cellular regime of DL instability
0
0.1
0.2
0.3
0.4
0.5
0
5
10
15
20
25
30
Time, t [ms]
 = 1.0
Ar 44 vol%
Flame radius, r [m]
Cellular regime
rc
Ar
Time, t [ms]
0
0.1
0.2
0.3
0.4
0.5
0
5
10
15
20
25
30
 = 1.0
Ar 0 vol%
Flame radius, r [m]
rc
Cellular regime
N2
Experiment
Laminar flame propagation (r = εSLt)

## Slide 11: Introduction - Flame front instabilities[3, 4][
Diffusional-thermal instability
caused by the preferential diffusion for non-equidiffusive mixtures
From small scale
Darrieus-Landau instability
From large scale
caused by the thermal volumetric expansion of burned gas
[3] F. A. Williams, Combustion Theory : Second Edition, Westview Press (1985).
[4] D. Bradley, et al., Flame acceleration due to flame-induced instabilities in large-scale explosions, Combustion and Flame 124, 2001, pp. 551-559
Two instabilities induce flame turbulence spontaneously.
On the other hand, thermal conduction stabilizes flame front.
When the deficient reactant diffuses faster, instability occurs.
Le < 1…The distabilizing effect due to non-equidiffusivity
Le > 1…The stabilizing effect due to themal conduction
Le =
α
D
α : The thermal diffusivity [m2/s]
D : The mass diffusivity of
deficient reactant [m2/s]
Ex. H2/Air : Instability is intensified at  < 1.0.

## Slide 12: Schlieren photography of laboratory-scale tests
 = 0.6
 = 1.8
N2
Ar
N2
Ar
The flame of  = 0.6 is remarkably unstable than that of  = 1.8, notwithstanding different inert gas.

## Slide 13: Results and discussions（Laboratory-scale）
✔  =0.6
✔  =1.0, 1.8
Flame acceleration by instability was not observed.
Flame acceleration by instability was observed.
Dimensionless burning velocity VS Dimensionless flame radius
vb : Burning velocity（measured value） [m/s]
ε : volumetric expansion ratio [-]
r : Flame radius [mm]
SL : Unstreched burning velocity [m/s]
δ : Laminar flame thickness [mm]
SL , δ, ε: calculated with CHEMKIN
r/δ [-]
vb/SL [-]
 = 0.6, ε = 5.62, N2
 = 0.6, ε = 6.85, Ar
 = 1.0, ε = 6.99, N2
 = 1.8, ε = 6.38, N2
 = 1.0, ε = 7.88, Ar
 = 1.8, ε = 7.27, Ar
0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
1.6
1.8
0
50
100
150
Flame propagation
is not accelerated.
Flame acceleration
Dimensionless burning velocity
Dimensionless flame radius,

## Slide 14: Results and discussions（Large-scale）
The lower  was, the more the flame acceleration was intensified due to diffusional-thermal instability. The effect of  on the flame acceleration was more remarkable than the effect of ε.
✔
Dimensionless burning velocity VS Dimensionless flame radius
SL , δ, ε: calculated with CHEMKIN
Flame acceleration
Flame propagation is not accelerated.
vb : Burning velocity（measured value） [m/s]
ε : volumetric expansion ratio [-]
r : Flame radius [mm]
SL : Unstreched burning velocity [m/s]
δ : Laminar flame thickness [mm]
 = 0.71, ε = 6.31, N2
 = 0.66, ε = 6.99, Ar
 = 1.03, ε = 7.13, N2
 = 1.02, ε = 8.06, Ar
 = 1.77, ε = 6.62, N2
 = 1.50, ε = 7.84, Ar
0
1
2
3
4
0
400
800
1200
1600
r/δ [-]
vb/SL [-]
Dimensionless burning velocity
Dimensionless flame radius,

## Slide 15: Results and discussions（Large-scale）
N2
Ar
0
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
 = 0.71
 = 0.66
 = 1.03
 = 1.02
 = 1.77
 = 1.50
ε = 6.31
ε = 7.13
ε = 6.62
ε = 6.99
ε = 8.06
ε = 7.84
Critical flame radius, rc [cm]
ε : volumetric expansion ratio[-]
rc : critical flame radius [cm]
 : equivalence ratio [-]
✔  ↓ … rc↓
✔ ε ↑ … rc↓
Diffusional-thermal instability promoted the onset of flame acceleration.
Or the effect of thermal conduction inhibited flame acceleration.
An increase in ε promoted the onset of flame acceleration.
The effect of ε on rc

## Slide 16: Results and discussions（Large-scale）
Blast wave
l : the distance from the ignition point
ε : the expansion ratio
ρ0 : the density of the medium
r : the flame radius
τ : the traveling time of blast wave
to the observed point
✔ At any equivalence ratio, the blast wave was greatly raised with an increase in Ar content ratio, because
the intensity of the blast wave depends on the square of the flame speed and the flame acceleration.
[2] A. Thomas, et al, Flame noise: Sound emission from spark-iginited bubbles of combustible gas, Pro. Roy. Soc. A294, 449- 466 (1966).
[2]
l = 3 m
-6
-4
-2
0
2
4
6
8
0
20
40
60
80
 = 0.71, Ar 0 vol%
 = 0.66, Ar 43 vol%
 = 1.03, Ar 0 vol%
 = 1.02, Ar 44 vol%
 = 1.77, Ar 0 vol%
 = 1.50, Ar 31 vol%
Overpressure, P [kPa]
Time, t [ms]

## Slide 17: Conclusions
Studies on gas explosions of H2-O2-N2-Ar mixtures were conducted in laboratory-scale and large-scale experiments.
✔
When expansion ratio was larger, the critical radius rc became smaller. This indicates that large expansion ratio promotes the onset of DL instability.
✔
It was found that the flame speed was more accelerated even if the flame scale was large at fuel lean condition, in which diffusional-thermal instability is effective.
✔
it was not easy to examine the effect of expansion ration on the dimensionless burning velocity in the experimental conditions performed in this study.
✔
The measured intensity of blast wave became much stronger when the flame was accelerated.
✔

## Slide 18
Thank you for your attention.

## Slide 19: Results and discussions（Large-scale）
0
5
10
15
20
25
30
35
0
500
1000
1500
2000
2500
Flame strech rate, K = (2/r)(dr/dt) [1/s]
Measured flame speed, dr/dt [m/s]
Defined critical flame radius
associated with onset of
self-accelerarion
Unstretched laminar flame speed
 = 1.03
Ar 0 vol%
Definition of rc[5]
K : Flame strech rate [1/s]
A : The flame surface area [m2]
Time, t [ms]
0
0.1
0.2
0.3
0.4
0.5
0
5
10
15
20
25
30
 = 1.03
Ar 0 vol%
Flame radius, r [m]
rc
The onset of flame acceleration
[5]Kim, W., Mogi, T., Kuwana, K., Dobashi, R., Self-similar propagation of expanding spherical flames in large scale gas explosions,
Proceedings of the Combustion Institute 35, 2015, pp. 2051-2018

## Slide 20: The definition of flame thickness
Tf : the flame temperature
Ti : unburned gas temperature
(dT/dx)max : maximum temperature gradient
[6] Law, C. and Sung, C., Structure, aerodynamics, and geometry of premixed flamelets, Progress in Energy and Combustion Science 26, 2000, pp. 2459-2505
[6]

## Slide 21: Experimental conditions of large-scale tests
 | Concentration [vol%] |  |  |  |  | ε | SL | δ | rc
 | H2 | O2 | N2 | Ar | [-] | [-] | [m/s] | [cm] | [cm]
A-1 | 23 | 16 | 61 | 0 | 0.71 | 6.31 | 1.11 | 0.0342 | 3.0
A-2 | 22 | 17 | 18 | 43 | 0.66 | 6.99 | 1.45 | 0.0341 | <1.0
B-1 | 30 | 15 | 55 | 0 | 1.03 | 7.13 | 2.16 | 0.0329 | 6.5
B-2 | 31 | 15 | 10 | 44 | 1.02 | 8.06 | 2.71 | 0.0348 | 4.5
C-1 | 43 | 12 | 45 | 0 | 1.77 | 6.62 | 2.70 | 0.0304 | 8.3
C-2 | 42 | 14 | 13 | 31 | 1.50 | 7.84 | 3.70 | 0.0328 | 6.0