## Slide 1
EXPERIMENTAL INVESTIGATION OF FLUID-STRUCTURE INTERACTION IN THE CASE OF HYDROGEN/AIR DETONATION IMPACTING A THIN PLATE
Alexis DANCELME
ICHS 2023- 20/09/2023
Co-authors :
Dr Sergey KUDRIAKOV
Dr Etienne STUDER
Dr Christian TENAUD

## Slide 2
Plan
Context and Experimental setup
Experimental results
Current and future work
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 3
Plan
Context and Experimental setup
Experimental results
Current and future work
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 4
CONTEXTE
 Risk linked to the presence of Hydrogen in a confined space
Detonation
Slow Deflagration
Fast Deflagration
Shock formation
Deflagration to detonation transition
H2 station accident
(South Korea, 2019)
CONTEXT
ICHS 2023- 20/09/2023 - Alexis Dancelme
      Real structure are very difficult for analysis
      A lot to learn for simple structure such as plate
      Study of the fluid-structure interaction in the case of detonation
      The pressure and impulse have a significant imapct on structure deformation

## Slide 5
CONTEXTE
 Risk linked to the presence of Hydrogen in a confined space
Detonation
Slow Deflagration
Fast Deflagration
Shock formation
Deflagration to detonation transition
H2 station accident
(South Korea, 2019)
CONTEXT
ICHS 2023- 20/09/2023 - Alexis Dancelme
      What is the influence of the plate deformation on the reflected shock (pressure and impulse)?
      Are the current models and correlation derived for solid explosive valid?

## Slide 6
Configuration with plate
SSEXHY EXPERIMENTAL FACILITY
ICHS 2023- 20/09/2023 - Alexis Dancelme
P3
P1
Instrumentations | Sensors
Photomultipliers | 14
Pressure sensors | 8
3 sections of 1310 mm long
Large spectrum of admissible pressure
Fluid Structure Interaction module
  Simple geometry : plate
  Control of initial Hydrogen concentration
    Study focused on mixture close to stoechiometry ()
P3
P1

## Slide 7
Scheme of a deformed plate
SSEXHY EXPERIMENTAL FACILITY
ICHS 2023- 20/09/2023 - Alexis Dancelme
  Simple geometry : plate
  Control of initial Hydrogen concentration
    Study focused on mixture close to stoechiometry ()
P3
P1
Plate after deformation and laser measurment

## Slide 8
Measurment on the plate, strain gages and laser
SSEXHY EXPERIMENTAL FACILITY
ICHS 2023- 20/09/2023 - Alexis Dancelme
Plate after deformation and laser measurment
  Simple geometry : plate
  Control of initial Hydrogen concentration
    Study focused on mixture close to stoechiometry ()
P3
P1
Fast frequency laser (100 kHz, )
Strain gages for large deformation

## Slide 9
16.6 cm
16.6 cm
METHODOLOGY
Pressure signals close to reflection
ICHS 2023- 20/09/2023 - Alexis Dancelme
Characterize pressure field at reflection
Reference signal for a non deformable material to study fluid-structure coupling

## Slide 10
Pressure signals close to reflection
METHODOLOGY
P3
P1
16.6 cm
16.6 cm
ICHS 2023- 20/09/2023 - Alexis Dancelme
Only P1 and P3 available
Uses of the reflected signal for comparison with non-deformable flange

## Slide 11
Plan
Context and Experimental setup
Experimental results
Current and future work
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 12
16.6 cm
16.6 cm
METHODOLOGY
All sensor on the full flange
ICHS 2023- 20/09/2023 - Alexis Dancelme
Homogeneity of the load on the flange

## Slide 13
EXPERIMENTAL RESULTS
Case | Thickness (mm) | Yield Strength (MPa) | (mol%) 0.2%
Plate 1 | 1.01 | 210 | 29.0
Plate 2 | 0.48 | 210 | 29.1
Plate 3 | 0.48 | 210 | 29.4
Plate 4 | 0.50 | 210 | 30.8
Plate 5 | 0.51 | 210 | 29.1
Plate 6 | 0.50 | 210 | 28.7
Plate 7 | 0.49 | 210 | 29.5
Plate 8 | 0.78 | 210 | 25.4
Plate 9 | 1 | 210 | 29.7
Plate 10 | 1 | 210 | 30.7
Case | Thickness (mm) | Yield Strength (MPa) | 
Plate 1 | 1.01 | 210 | 29.0
Plate 2 | 0.48 | 210 | 29.1
Plate 3 | 0.48 | 210 | 29.4
Plate 4 | 0.50 | 210 | 30.8
Plate 5 | 0.51 | 210 | 29.1
Plate 6 | 0.50 | 210 | 28.7
Plate 7 | 0.49 | 210 | 29.5
Plate 8 | 0.78 | 210 | 25.4
Plate 9 | 1 | 210 | 29.7
Plate 10 | 1 | 210 | 30.7
ICHS 2023- 20/09/2023 - Alexis Dancelme
  Test matrix for thin plate at
Experimental campaign for thin plate

## Slide 14
Impulse comparison for P1 sensor
EXPERIMENTAL RESULTS
P3
P1
16.6 cm
16.6 cm
ICHS 2023- 20/09/2023 - Alexis Dancelme
Good repeatability before reflection

## Slide 15
Impulse comparison for P1 sensor
EXPERIMENTAL RESULTS
P3
P1
16.6 cm
16.6 cm
ICHS 2023- 20/09/2023 - Alexis Dancelme
Systematic decay in impulse
Reference pressure define as pressure just before the reflected shock arrival

## Slide 16
EXPERIMENTAL RESULTS
Relative impulse for P1
Systematic reduction of impulse of the order of 15%
P3
P1
16.6 cm
16.6 cm
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 17
EXPERIMENTAL RESULTS
Case | Centre displacement (mm) | Thickness (mm) | Yield Strength (MPa) | Displacement to thickness ratio | (mol%)
Plate 1 | 9.4 | 1.01 | 210 | 9.3 | 29.0
Plate 2 | 17.7 | 0.48 | 210 | 36.9 | 29.1
Plate 3 | 16.8 | 0.48 | 210 | 35.2 | 29.4
Plate 4 | 19.8 | 0.50 | 210 | 39.6 | 30.8
Plate 5 | 18.1 | 0.51 | 210 | 35.5 | 29.1
Plate 6 | 18.4 | 0.50 | 210 | 36.8 | 28.7
Plate 7 | 17.4 | 0.49 | 210 | 35.5 | 29.5
Plate 8 | 11.8 | 0.78 | 210 | 15.13 | 25.4
Plate 9 | 10.3 | 1 | 210 | 10.3 | 29.7
Plate 10 | 10.0 | 1 | 210 | 10 | 30.7
Case | Centre displacement (mm) | Thickness (mm) | Yield Strength (MPa) | Displacement to thickness ratio | 
Plate 1 | 9.4 | 1.01 | 210 | 9.3 | 29.0
Plate 2 | 17.7 | 0.48 | 210 | 36.9 | 29.1
Plate 3 | 16.8 | 0.48 | 210 | 35.2 | 29.4
Plate 4 | 19.8 | 0.50 | 210 | 39.6 | 30.8
Plate 5 | 18.1 | 0.51 | 210 | 35.5 | 29.1
Plate 6 | 18.4 | 0.50 | 210 | 36.8 | 28.7
Plate 7 | 17.4 | 0.49 | 210 | 35.5 | 29.5
Plate 8 | 11.8 | 0.78 | 210 | 15.13 | 25.4
Plate 9 | 10.3 | 1 | 210 | 10.3 | 29.7
Plate 10 | 10.0 | 1 | 210 | 10 | 30.7
ICHS 2023- 20/09/2023 - Alexis Dancelme
  Experimental campaign for thin plate at
Experimental campaign for thin plate

## Slide 18
    Plate deformation
      Solid explosive1
1 G.N. Nurick, Deformation of Thin Plates subjected to impulsive loading – Part I, II, III (1989, 1989, 2016)
Plate
Explosive
Scheme of a plate with an explosive sheet
h
EXPERIMENTAL RESULTS
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 19
EXPERIMENTAL RESULTS
Case | Centre displacement (mm) | Thickness (mm) | Yield Strength (MPa) | Displacement to thickness ratio | Impulsion corresponding to Nurick’s correlation (bar.s)
Plate 1 | 9.4 | 1.01 | 210 | 9.3 | 0.0046
Plate 2 | 17.7 | 0.48 | 210 | 36.9 | 0.0042
Plate 3 | 16.8 | 0.48 | 210 | 35.2 | 0.0040
÷2
x4
ICHS 2023- 20/09/2023 - Alexis Dancelme
Comparison of the experimental results with the Nurick’s correlation

## Slide 20
Impulsion mesurée à la bride
Impulse reached after ~ 0.2 ms
EXPERIMENTAL RESULTS
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 21
EXPERIMENTAL RESULTS
P3
P1
16.6 cm
16.6 cm
Measured deformation time ~0.2-0.25 ms
Strain gage and laser signal
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 22
Plan
Context and Experimental setup
Experimental results
Current and future work
ICHS 2023- 20/09/2023 - Alexis Dancelme

## Slide 23
CURRENT AND FUTURE WORK

## Slide 24
  Homogemous load at reflection in the case of detonation
  Characterize the fluid-structure coupling with a systematic decay of 15% in impulse after reflection
  Applicability of Nurick’s correlation based on solid explosive to find impulse at reflection and deformation time
  Numerical simulation catches the important characterisics for displacement
  Perspectives
    Experimental : Statistical analysis of the deformed shape
    Experimental : Extension to fast flame (higher deformation for lean mixture)
    Converging to a coupled approach for the simulation
CONCLUSION

## Slide 25: Thanks for your attention! Any questions?
25